## Slide 1: IPv4 Addressing Overview V1.0

## Slide 2: The Structure of the IP Address

## Slide 3: IPV4 Network Public Addresses – Structure
Class A
  Range 1.0.0.0 to 127.0.0.0, 1 to 127
  Default mask 255.0.0.0, /8
  Structure N.H.H.H
  Who Owns ?
    19.0.0.0/8 Ford Motor Company (USA)
    56.0.0.0/8 US Postal Service (USA)
    36.0.0.0/8 Stanford University (USA)

## Slide 4: IPV4 Network Public Addresses – Structure
Class B
  Range 128.0.0.0 to 191.255.0.0, 128 to 191
  Default mask 255.255.0.0, /16
  Structure N.N.H.H
  Who Owns ? (Whois)
    136.185.0.0/16 Telenor Communications Pvt. Ltd. (India)
    136.186.0.0/16 Swinburne University (Australia)
    136.187.0.0/16 National Institute of Informatics (Japan)

## Slide 5: IPV4 Network Public Addresses – Structure
Class C
  Range 192.0.0.0 to 223.255.255.0, 192 to 223
  Default mask 255.255.255.0, /24
  Structure N.N.N.H
  Who Owns ?
    198.32.10.0/24 Almond Oil Process, LLC.. (USA)
    200.25.35.0/24 Telecorp S.A. (Colombia)
    205.60.57.0/24 Navy Network Information Center (USA)

## Slide 6: IPV4 Network Public Addresses – Structure
Class A – Example
  N.H.H.H
  36.0.0.0/8
  Default mask 255.0.0.0
  Network address 36.0.0.0
  Host IP address range 36.0.0.1 to 36.255.255.254
  Broadcast Address 36.255.255.255

## Slide 7: IPV4 Network Public Addresses – Structure
Class B – Example
  N.N.H.H
  136.186.0.0/16
  Default mask 255.255.0.0
  Network address 136.186.0.0
  Host IP address range 136.186.0.1 to 136.186.255.254
  Broadcast Address 136.186.255.255

## Slide 8: IPV4 Network Public Addresses – Structure
Class C – Example
  N.N.N.H
  205.60.57.0/24
  Default mask 255.255.255.0
  Network address 205.60.57.0
  Host IP address range 205.60.57.1 to 205.60.57.254
  Broadcast Address 205.60.57.255

## Slide 9: Identifying IP Address Exercise

## Slide 10: Identifying Types of IP Address
The 4 Definitions
A Network IP Address is when
  All host binary bits are set to zeros (0s) and the mask is default mask for the class
A Subnet IP Address is when
  All host binary bits are set to zeros (0s) and the mask is greater than default mask for the class
A Host IP Address is when
  At least one binary host bit is set to one (1)
A Broadcast IP Address is when
  All binary hosts bits are set to ones (1s)

## Slide 11: Identifying Types of IP Address
Given IP Address 148.29.0.65/27
1.What is its Class: B
2. What is its Default Prefix and Mask: /16, 255.255.0.0
3. What is its Default Structure: N.N.H.H
4. What is its current Prefix and Mask: /27, 255.255.224
5. How many bits allocate to subnetting: 27 - 16 = 11 bits
6. Show structure – subnet part, host part
148.29.00000000.00000000
7. In given IP address convert decimal values in subnet and host parts to binary
148.29.00000000.01000001
8. What Type of Address ? refer The 4 Definitions

## Slide 12: Identifying Types of IP Address
IP Address 145.17.0.0/16
IP Address 120.0.25.0/8
IP Address 193.16.36.64/26
IP Address 144.61.2.0/18
IP Address 105.0.32.0/19
IP Address 201.33.18.31/28

## Slide 13: Identifying Types of IP Address
IP Address 148.29.0.65/27
IP Address 93.33.25.0/11
IP Address 214.16.51.31/26
IP Address 159.23.20.0/21
IP Address 75.0.32.23/21
IP Address 201.22.61.64/28

## Slide 14: Subnet Exercises Usable Host Range A Specified Usable Host Broadcast

## Slide 15: Subnet Exercises
For each of the following subnets, find
  Usable Host Range, Broadcast address and the specified usable IP Host Address:
    152.18.0.64/27, Find 6th usable
    45.64.0.0/11, Find 200th usable
    202.116.29.128/26, Find 13th usable
    138.211.32.0/21, Find 300th usable
    39.64.0.0/19, Find 400th usable
    193.44.100.64/28, Find 12th usable

## Slide 16: Partitioning IP Addresses Exercise

## Slide 17: Partitioning IP Address Space
Partition Network Address space 173.74.0.0/16 into two parts
  Current 173.74./00000000.00000000 prefix /16
  To partition into two parts change prefix to /17 173.74.0/0000000.00000000
    Partition 1 173.74.00000000.00000000 /17 (173.74.0.0/17)
    Partition 2 173.74.10000000.00000000 /17 (173.74.128.0/17)
Partition Network Address space 153.85.0.0/16 into four parts
  Current 153.85./00000000.00000000 prefix /16
  To partition into four parts change prefix to /18 153.74.00/000000
    Partition 1 153.85.00000000.00000000 /18 (153.85.0.0/18)
    Partition 2 153.85.01000000.00000000 /18 (153.85.64.0/18)
    Partition 3 153.85.10000000.00000000 /18 (153.85.128.0/18)
    Partition 4 153.85.11000000.00000000 /18 (153.85.192.0/18)

## Slide 18: Partitioning IP Address Space Exercises
Partition Network Address space 156.34.0.0/16 into two parts
Partition Network Address space 144.52.0.0/16 into four parts
  What is the broadcast address for partition 2
Partition Network Address space 138.63.0.0/18 into two parts
Partition Network Address space 166.25.0.0/20 into four parts
  What is the host range for partition 3
Partition Network Address space 193.73.27.0/24 into two parts
Partition Network Address space 206.15.39.64/26 into two parts
  What is the broadcast address for partition 1
Partition Network Address space 110.64.0.0/19 into two parts
Partition Network Address space 44.16.0.0/21 into four parts
  What is the host address range for partition 3

## Slide 19: Subnetting Exercise Fixed Length Subnet Mask FLSM
Select the LAN subnet with the largest number of hosts.
Select the mask that provides sufficient IP addresses for this LAN subnet
Use this mask for all the other subnets

## Slide 20
R1
R2
R3
LAN D
LAN B
LAN C
LAN A
LAN E
S1
S2
Subnet | Number of Hosts
LAN A | 200
LAN B | 150
LAN C | 100
LAN D | 50
LAN E | 30
S1 | 2
S2 | 2
136.186.0.0/16

## Slide 21
Subnetting Table |  |  | 
Mask | Prefix | Nos Host Bits | Nos Hosts
 |  | 20 | 1
 |  | 21 | 2
255.255.255.252 | (32-2) -> /30 | 22 | 4
255.255.255.248 | (32-3) -> /29 | 3 | 8
255.255.255.240 | (32-4) -> /28 | 4 | 16
255.255.255.224 | (32-5) -> /27 | 5 | 32
255.255.255.192 | (32-6) -> /26 | 6 | 64
255.255.255.128 | (32-7) -> /25 | 7 | 128
255.255.255.0 | (32-8) -> /24 | 8 | 256
255.255.254.0 | (32-9) -> /23 | 9 | 512
255.255.252.0 | (32-10) -> /22 | 10 | 1024
255.255.248.0 | (32-11) -> /21 | 11 | 2048
255.255.240.0 | (32-12) -> /20 | 12 | 4096
255.255.224.0 | (32-13) -> /19 | 13 | 8192
255.255.192.0 | (32-14) -> /18 | 14 | 16384
Subnet | Subnet Network Address | Prefix
LAN A |  | 
LAN B |  | 
LAN C |  | 
LAN D |  | 
LAN E |  | 
S1 |  | 
S2 |  | 
136.186.0.0/16

## Slide 22
Subnetting Exercise Variable Length Subnet Mask VLSM
Starting with the LAN subnet that has the largest number of hosts.
  Select the mask that provides sufficient IP addresses for this LAN subnet
  Use this mask only for this subnet
  If more subnets then, else go to 4
    Starting with the LAN subnet that has the next largest number of hosts.
    Go to 1
  No More subnets

## Slide 23
R1
R2
R3
LAN D
LAN B
LAN C
LAN A
LAN E
S1
S2
Subnet | Number of Hosts
LAN A | 800
LAN B | 260
LAN C | 100
LAN D | 50
LAN E | 30
S1 | 2
S2 | 2
165.51.0.0/16

## Slide 24
Subnetting Table |  |  | 
Mask | Prefix | Nos Host Bits | Nos Hosts
 |  | 20 | 1
 |  | 21 | 2
255.255.255.252 | (32-2) -> /30 | 22 | 4
255.255.255.248 | (32-3) -> /29 | 3 | 8
255.255.255.240 | (32-4) -> /28 | 4 | 16
255.255.255.224 | (32-5) -> /27 | 5 | 32
255.255.255.192 | (32-6) -> /26 | 6 | 64
255.255.255.128 | (32-7) -> /25 | 7 | 128
255.255.255.0 | (32-8) -> /24 | 8 | 256
255.255.254.0 | (32-9) -> /23 | 9 | 512
255.255.252.0 | (32-10) -> /22 | 10 | 1024
255.255.248.0 | (32-11) -> /21 | 11 | 2048
255.255.240.0 | (32-12) -> /20 | 12 | 4096
255.255.224.0 | (32-13) -> /19 | 13 | 8192
255.255.192.0 | (32-14) -> /18 | 14 | 16384
Subnet | Subnet Network Address | Prefix
LAN A |  | 
LAN B |  | 
LAN C |  | 
LAN D |  | 
LAN E |  | 
S1 |  | 
S2 |  | 
165.51.0.0/16

## Slide 25
Tree Method

## Slide 26
Subnet Name | Needed Size | Allocated Size | Address | Mask | Dec Mask | Assignable Range | Broadcast
A | 800 | 1022 | 165.51.0.0 | /22 | 255.255.252.0 | 165.51.0.1 - 165.51.3.254 | 165.51.3.255
B | 260 | 510 | 165.51.4.0 | /23 | 255.255.254.0 | 165.51.4.1 - 165.51.5.254 | 165.51.5.255
C | 100 | 126 | 165.51.6.0 | /25 | 255.255.255.128 | 165.51.6.1 - 165.51.6.126 | 165.51.6.127
D | 50 | 62 | 165.51.6.128 | /26 | 255.255.255.192 | 165.51.6.129 - 165.51.6.190 | 165.51.6.191
E | 30 | 30 | 165.51.6.192 | /27 | 255.255.255.224 | 165.51.6.193 - 165.51.6.222 | 165.51.6.223
S1 | 2 | 2 | 165.51.6.224 | /30 | 255.255.255.252 | 165.51.6.225 - 165.51.6.226 | 165.51.6.227
S2 | 2 | 2 | 165.51.6.228 | /30 | 255.255.255.252 | 165.51.6.229 - 165.51.6.230 | 165.51.6.231
Subnetting Successful VLSM
Major Network: 165.51.0.0/16 Available IP addresses in major network: 65534 Number of IP addresses needed: 1244 Available IP addresses in allocated subnets: 1754 About 3% of available major network address space is used About 71% of subnetted network address space is used
VLSM Calculator http://www.vlsm-calc.net/

## Slide 27: VLSM Exercises 1
135.20.0.0/16 A - 2000, B – 350, C – 300, D – 110, E – 20, S1 – 2, S2 - 2
176.20.0.0/18 A - 500, B – 200, C – 150, D – 50, E – 50, S1 – 2, S2 – 2
133.72.0.0/17 A - 1000, B – 200, C – 150, D – 50, E – 20, S1 – 2, S2 – 2
153.12.0.0/19 A - 400, B – 100, C – 50, D – 20, E – 20, S1 – 2, S2 – 2
182.111.0.0/20 A - 1000, B – 200, C – 100, D – 60, E – 60, S1 – 2, S2 – 2
163.222.0.0/21 A - 500, B – 200, C – 100, D –100, E – 60, S1 – 2, S2 – 2

## Slide 28: VLSM Exercises 2
145.60.128.0/17 A - 5000, B – 350, C – 300, D – 45, E – 20, S1 – 2, S2 - 2
156.15.64.0/18 A - 1500, B – 200, C – 150, D – 100, E – 100, S1 – 2, S2 – 2
148.96.32.0/19 A - 1000, B – 200, C – 150, D – 50, E – 20, S1 – 2, S2 – 2
173.128.16.0/20 A - 1500, B – 100, C – 50, D – 20, E – 20, S1 – 2, S2 – 2
187.201.32.0/21 A - 1000, B – 200, C – 200, D – 60, E – 20, S1 – 2, S2 – 2
135.166.8.0/22 A - 500, B – 100, C – 50, D – 25, E – 25, S1 – 2, S2 – 2